## Slide 1: EECS 489 Computer Networks Fall 2020
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
Introductions
Class policies, logistics, and roadmap
Overview of the basics
  How is the network shared?
  How do we evaluate a network?
  What is a network made of?

## Slide 3: GSIs
Office hours: See course webpage
Jie You
Joseph Buiteweg

## Slide 4: Mosharaf Chowdhury
At Michigan since 2016
Research focus on application-infrastructure symbiosis in large-scale networked systems
Office hours: Wednesday 2PM – 3:15PM in 4820 BBB
  Queue: https://officehours.it.umich.edu/queue/421
  Also, by appointment (pre-scheduled via email)
Lectures will be recorded (but not discussions)
Ask questions in chat

## Slide 5: 489 in EECS curriculum
EECS 281
  High-level logic ⇒ Programs
  Coding skills learned in 281 are critical for 489 assignments
EECS 482
  How do machines work?
  Execute programs, interact with users, etc.
  Prior 482 experience is not needed

## Slide 6: What is missing?
How do we access most services?
  Examples include search engines, social networks, video streaming, etc.
How do two machines communicate?
  When they are directly connected
  When they are not directly connected
Using a network

## Slide 7: What is a network?
A system of “links” that interconnect “nodes” in order to move “information” between nodes
We will focus primarily on the Internet

## Slide 8: What is EECS 489 about?
To learn about (at a high level)
  How the Internet works
  Why it works the way it does
  How to reason about complicated design problems
What it’s not about
  How to write web services
  How to design web pages
  …

## Slide 9: Class workload
Four assignments
  First one is an individual assignment
  The rest are in groups of 3
Exams:
  Midterm: October 19
  Final: December 16 8 AM – 10 AM

## Slide 10: Grading
 | Allocation
Assignment 1 | 5%
Assignment 2 | 15%
Assignment 3 | 15%
Assignment 4 | 15%
Midterm | 25%
Final | 25%
Bonus Quizzes | 2%

## Slide 11: The ALL-NEW* assignments
Assignment 1: measure end-to-end throughput and delay of networks (i.e., simple speed test)
Assignment 2: video streaming from CDNs (i.e., simple Netflix)
Assignment 3: reliable transport (i.e., how to transfer data over an unreliable network)
Assignment 4: router design (i.e., how do internal elements of the network work)
All on (emulated) realistic networks using mininet

## Slide 12: Bonus Quizzes
10 MCQ and solution key for each of the 20 lectures
Made online sometime after the lecture; live for 48 hours
Participation counts for 0.1 on top of your final grade
  Max 2.0
How well you do doesn’t matter
Prepared over the summer by Tejaswi
Tejaswi Worlikar

## Slide 13: Enrollment and wait list
Wait-listed students will be admitted in the order of wait list
If you’re planning to drop, please do so soon!

## Slide 14: Communication protocol
Course website: http://mosharaf.com/eecs489/
  Assignments, lecture slides
Confidential content on canvas
Piazza for all communication
  Sign up if you haven’t already
  https://piazza.com/umich/fall2020/eecs489/
Assignment submission via Github
  Start forming groups
  Details will be sent out soon

## Slide 15: Policies on late submission, re-grade request, cheating …
Detailed description in the course webpage
Don’t cheat!

## Slide 16: Let’s Talk Internet

## Slide 17: The Internet consists of many end-systems
end-system
Windows PC
Linux server
MAC laptop
car navigator
heart pacemaker
smartphone
iPad

## Slide 18: Connected by switches
switch
end-system

## Slide 19: And links
phone lines
link
fibers
cable TV lines
wireless links
switch
end-system

## Slide 20: Managed by many parties
Internet Service Provider
phone company
cable company
university net
link
switch
end-system

## Slide 21: Transfers data
switch
data
path
Internet Service Provider
link
end-system

## Slide 22: A federated system
The Internet ties together different networks by the IP protocol
  A common interface binds them all together
Google
Fiber
AT&T
Comcast

## Slide 23: Switched networks
End-systems and networks connected by switches instead of directly connecting them
  Why?
Allows us to scale
  For example, directly connecting N nodes to each other would require N2 links!

## Slide 24: When do we need to share the network?
Switch and link resources

## Slide 25: Shared among many services
Zoom client
Zoom client
Facebook server
Firefox accessing Facebook
Fortnite client
Fortnite server

## Slide 26: Two ways to share switched networks
Circuit switching
  Resource reserved per connection
  Admission control: per connection
Packet switching via statistical multiplexing
  Packets treated independently, on-demand
  Admission control: per packet

## Slide 27: Circuit switching
src sends reservation request to dst
Switches create circuit after admission control
src sends data
src sends teardown request
More details in backup
dst
src
10 Mbps?
10 Mbps?
✔️
✔️

## Slide 28: Circuit switching
Reservation establishes a “circuit” within a switch
switch
src
dst

## Slide 29: Circuit switching
Pros
  Predictable performance
  Simple/fast switching (once circuit established)
Cons
  Complexity of circuit setup/teardown
  Inefficient when traffic is bursty
  Circuit setup adds delay
  Switch fails  its circuit(s) fails

## Slide 30: Packet switching
Each packet contains destination (dst)
Each packet treated independently
switch
dst

## Slide 31: Packet switching
Each packet contains destination (dst)
Each packet treated independently
With buffers to absolve transient overloads
switch
dst

## Slide 32: Packet switching
Pros
  Efficient use of network resources
  Simpler to implement
  Robust: can “route around trouble”
Cons
  Unpredictable performance
  Requires buffer management and congestion control

## Slide 33: Statistical multiplexing
Allowing more demands than the network can handle
  Hoping that not all demands are required at the same time
  Results in unpredictability
  Works well except for the extreme cases

## Slide 34: 5-minute break!

## Slide 35: How do we evaluate a network?

## Slide 36: Performance metrics
Delay
Loss
Throughput

## Slide 37: Delay
How long does it take to send a packet from its source to destination?

## Slide 38: Delay
Consists of four components
  Transmission delay
  Propagation delay
  Queuing delay
  Processing delay
due to link properties
due to traffic mix and
switch internals

## Slide 39: A network link
Link bandwidth
  Number of bits sent/received per unit time (bits/sec or bps)
Propagation delay
  Time for one bit to move through the link (seconds)
bandwidth
Propagation delay
delay x bandwidth

## Slide 40: 1. Transmission delay
How long does it take to push all the bits of a packet into a link?
Packet size / Transmission rate of the link
  E.g., 1000 bits / 100 Mbits per sec = 10-5 sec

## Slide 41: 2. Propagation delay
How long does it take to move one bit from one end of a link to the other?
Link length / Propagation speed of link
  E.g., 30 kilometers / 3*108 meters per sec = 10-4 sec

## Slide 42: Packet delay Sending a 100-byte packet
time=0
A
B
100Byte packet
Time
1Mbps, 1ms
Time to transmit one bit = 1/106s
Time to transmit 800 bits=800x1/106s
Time when that bit reaches B = 1/106+1/103s
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms

## Slide 43: Packet delay Sending a 100-byte packet
time=0
A
B
100Byte packet
Time
1Gbps, 1ms
Time to transmit one bit = 1/109s
Time to transmit 800 bits=800x1/109s
Time when that bit reaches B = 1/109+1/103s
The last bit reaches B at
(800x1/109)+1/103s
= 1.0008ms

## Slide 44: Sending a large file using 100-byte packets
100Byte packet
100Byte packet
A
B
100Byte packet
1Gbps, 1ms

## Slide 45: Pipe view of a link
Transmission delay decreases as bandwidth increases
time
bandwidth
transmission delay

## Slide 46: 3. Queuing delay
How long does a packet have to sit in a buffer before it is processed?

## Slide 47: Queueing delay: “pipe” view

## Slide 48: Queueing delay: “pipe” view
No overload!

## Slide 49: Queueing delay: “pipe” view
Transient Overload
Not a rare event!
Queue

## Slide 50: Queueing delay: “pipe” view
Queue
Transient Overload

## Slide 51: Queueing delay: “pipe” view
Queue
Transient Overload

## Slide 52: Queueing delay: “pipe” view
Queue
Transient Overload

## Slide 53: Queueing delay: “pipe” view
Queue
Transient Overload

## Slide 54: Persistent overload leads to packet drop/loss
Queue

## Slide 55: Queueing delay
How long does a packet have to sit in a buffer before it is processed?
Depends on traffic pattern
  Arrival rate at the queue
  Nature of arriving traffic (bursty or not?)
  Transmission rate of outgoing link

## Slide 56: Queueing delay
How long does a packet have to sit in a buffer before it is processed?
Characterized with statistical measures
  Average queuing delay
  Variance of queuing delay
  Probability delay exceeds a threshold value

## Slide 57: Basic queueing theory terminology
Arrival process: how packets arrive
  Average rate A
W: average time packets wait in the queue
  W for “waiting time”
L: average number of packets waiting in the queue
  L for “length of queue”

## Slide 58: Little’s Law (1961)
L = A x W
Compute L: count packets in queue every second
Why do you care?
  Easy to compute L, harder to compute W
Notes: Row vs column

## Slide 59: 4. Processing Delay
How long does the switch take to process a packet?
  Negligible

## Slide 60: End-to-end delay
transmission
propagation
queueing
processing
transmission
propagation
queueing
processing
transmission
propagation

## Slide 61: Round Trip Time (RTT)
Time for a packet to go from a source to a destination and to come back
Why do we care?
  Measuring delay is hard from one end
RTT/2 equals average end-to-end delay
  Why not exact?

## Slide 62: Loss
What fraction of the packets sent to a destination are dropped?

## Slide 63: Throughput
At what rate is the destination receiving data from the source

## Slide 64: Throughput
F/R + propagation delay
Transmission rate R bits/sec
Average throughput =
Transfer time (T) =
File of size F bits
F/T ≈ R
Packets of size L bits

## Slide 65: End-to-end throughput
Transmission rate R
File of size F bits
Packets of size L bits
Transmission rate R’ > R
Average throughput =
min{R, R’} = R
bottleneck link

## Slide 66: Summary
How is the network shared?
  On-demand or via reservation
How do we evaluate a network?
  Bandwidth, delay, loss, …
What is a network made of?
  Whatever physical infrastructure exist
  See backup slides

## Slide 68: What is the network made of?

## Slide 69: What is a network made of?
link
switch
end-system
Internet Service Provider

## Slide 70: What is a network made of?
phone company

## Slide 71: What is a network made of?
phone company

## Slide 72: The last hop
home PC
switch

## Slide 73: How do we connect?
home PC
switch
DSL modem
DSLAM
central office
phone line
telephone
telephone network
...
Notes: DSLAM: Digital Subscriber Line Access Multiplexer

## Slide 74: Digital Subscriber Line (DSL)
Twisted pair copper
3 separate channels
  downstream data channel
  upstream data channel
  2-way phone channel
up to 25 Mbps downstream
up to 2.5 Mbps upstream

## Slide 75: How about an cable provider as an ISP?
cable company

## Slide 76: Connecting via cable
home PC
switch
cable modem
CMTS
cable head end
copper
fiber
...
Notes: CMTS: Cable Modem Termination System

## Slide 77: Cable
Coaxial copper & fiber
Up to 42.8 Mbps downstream
Up to 30.7 Mbps upstream
Shared broadcast medium

## Slide 78: Any other means?
university net

## Slide 79: Ethernet
workstation
“aggregate” switch
Ethernet cable
“local” switch
...

## Slide 80: Ethernet
Twisted pair copper
100 Mbps, 1 Gbps, 10 Gbps (each direction)

## Slide 81: Many other ways
Cellular (smart phones)
Satellite (remote areas)
Fiber to the Home (home)
Optical carrier (Internet backbone)

## Slide 82: Where is WiFi?
WiFi
WiFi
WiFi

## Slide 84: MASSIVE Scale
4.6 Billion users
>1.8 Billion websites
>200 Billion emails sent per day
>2.5 Billion smartphones
>2.7 Billion Facebook users
>1 Billion hours of YouTube watched per day
Routers that switch 10 Terabits/second
Links that carry 100 Gigabits/second
Notes: https://www.internetlivestats.com

## Slide 85: Have we found the right solution?
We don’t really know
What we do know
  The early Internet pioneers came up with a solution that was successful beyond all imagining
  Several enduring architectural principles and practices emerged from their work
Still, it is just one design with many questions

## Slide 86: The Internet is a lesson
In how to reason through the design of a very complex system
  What are our goals and constraints?
  What’s the right prioritization of goals?
  How do we decompose a problem?
  Who does what? How?
  What are the interfaces between components?
  What are the tradeoffs between design options?

## Slide 87: Details on Circuit Switching

## Slide 88: Many kinds of circuits
Time division multiplexing
  divide time in time slots
  separate time slot per circuit
Frequency division multiplexing
  divide frequency spectrum in frequency bands
  separate frequency band per circuit
time
time
frequency

## Slide 89: Timing in circuit switching
time

## Slide 90: Timing in circuit switching
time

## Slide 91: Timing in circuit switching
time

## Slide 92: Timing in circuit switching
time

## Slide 93: Timing in circuit switching
time
Circuit establishment

## Slide 94: Timing in circuit switching
Data
time
Circuit establishment
Data transfer

## Slide 95: Timing in circuit switching
Data
time
Circuit establishment
Data transfer
Circuit teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 96: Why the delays?
Data
time
Circuit establishment
Data transfer
Circuit teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 97: Timing in circuit switching
time
Circuit establishment
Data transfer
Circuit teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 98: Timing in circuit switching
Data
time
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 99: Timing in circuit switching
time
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 101: A network link: BDP
Link bandwidth
  Number of bits sent/received per unit time (bits/sec or bps)
Propagation delay
  Time for one bit to move through the link (seconds)
Bandwidth-Delay Product (BDP)
  Number of bits “in flight” at any time
BDP = bandwidth × propagation delay
bandwidth
Propagation delay
delay x bandwidth

## Slide 102: BDP Examples
Same city over a slow link:
  Bandwidth: ~100Mbps
  Propagation delay: ~0.1msec
  BDP: 10,000bits (1.25KBytes)
Cross-country over fast link:
  Bandwidth: ~10Gbps
  Propagation delay: ~10msec
  BDP: 108bits (12.5MBytes)