## Slide 1: EECS 489 Computer Networks Fall 2020
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Topics
Basics (lectures 1–2)
Application layer (lectures 3–5)
  HTTP, DNS, and CDN
  Video Streaming

## Slide 3: Basic concepts
You should know:
  Packet vs. circuit switching
  Statistical multiplexing
  Link characteristics
  Packet delays

## Slide 4: Switched networks
End-systems and networks connected by switches instead of directly connecting them
Allows us to scale
  For example, directly connecting N nodes to each other would require N2 links!

## Slide 5: How are network resources shared?
Two approaches
  Reservations  circuit switching
  On-demand  packet switching

## Slide 6: Two approaches to sharing
Packet switching
  Network resources consumed on demand per-packet
  Admission control: per packet
Circuit switching
  Network resources reserved a priori at “connection” initiation
  Admission control: per connection

## Slide 7: Circuit switching
src sends reservation request to dst
Switches create circuit after admission control
src sends data
src sends teardown request
dst
src
10 Mbps?
10 Mbps?
✔️
✔️

## Slide 8: Packet switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”
Switches “forward” packets based on their headers
Each packet travels independently
No link resources are reserved

## Slide 9: Statistical multiplexing
Allowing more demands than the network can handle
  Hoping that not all demands are required at the same time
  Good for bursty traffic (average << peak demand)
  Packet switching exploits statistical multiplexing better than circuit switching

## Slide 10: Performance metrics
Delay
Loss
Throughput

## Slide 11: Delay
Consists of four components
  Transmission delay
  Propagation delay
  Queuing delay
  Processing delay
due to link properties
due to traffic mix and
switch internals

## Slide 12: A network link
Link bandwidth
  Number of bits sent/received per unit time (bits/sec or bps)
Propagation delay
  Time for one bit to move through the link (seconds)
bandwidth
Propagation delay
delay x bandwidth

## Slide 13: Queueing delay
How long does a packet have to sit in a buffer before it is processed?
Characterized with statistical measures
  Average queuing delay
  Variance of queuing delay
  Probability delay exceeds a threshold value

## Slide 14: End-to-end delay
transmission
propagation
queueing
processing
transmission
propagation
queueing
processing
transmission
propagation

## Slide 15: What we want
http://123.xyz
123.xyz server

## Slide 16: (Some of) What happens…
5.6.7.*
host
host
host
...
5.6.7.8
1.2.3.*
host
host
DNS
...
router
router
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 17: (More of) What happens
5.6.7.*
host
host
host
...
5.6.7.8
1.2.3.*
host
host
DNS
...
router
router
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 18: What we get
http://123.xyz
123.xyz server
Hello

## Slide 19: Layers
Layer: a part of a system with well-defined interfaces to other parts
One layer interacts only with layer above and layer below
Two layers interact only through the interface between them

## Slide 20: Layers in practice
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch
Notes: Why go up? Why not stay down in the lower levels?

## Slide 21: Layer encapsulation: Protocol headers
TCP header
IP header
Ethernet
header
HTTP
request/response
User A
User B
Notes: Deepest level most header

## Slide 22: IP is the narrow waist of the layering hourglass
SMTP
HTTP
TCP
UDP
IP
PPP
FDDI
Ethernet
PSTN
Radio
Copper
Optical
NTP
DNS

## Slide 23: Placing network functionality
End-to-end arguments by Saltzer, Reed, and Clark
  Dumb network and smart end systems
  Functions that can be completely and correctly implemented only with the knowledge of application end host, should not be pushed into the network
  Sometimes necessary to break this for performance and policy optimizations
  Fate sharing: fail together or don’t fail at all

## Slide 24: 5-minute break!

## Slide 25: Topics
Basics (lectures 1–2)
Application layer (lectures 3–5)
  HTTP, DNS, and CDN
  Video Streaming

## Slide 26: Hyper Text Transfer Protocol (HTTP)
Client-server architecture
  Server is “always on” and “well known”
  Clients initiate contact to server
Synchronous request/reply protocol
  Runs over TCP, Port 80
Stateless
ASCII format
  Before HTTP/2

## Slide 27: Steps in HTTP request/response
Client
Server
TCP syn
TCP syn + ack
TCP ack + HTTP GET
.
.
.
Establish
connection
Request
response
Client
request
Close connection

## Slide 28: Object request response time
RTT (round-trip time)
  Time for a small packet to travel from client to server and back
Response time
  1 RTT for TCP setup
  1 RTT for HTTP request and first few bytes
  Transmission time
  Total = 2RTT + Transmission Time
Client
Server
TCP syn
TCP syn + ack
TCP ack + HTTP GET
RTT
RTT
Tx

## Slide 29: Improving HTTP performance
Optimizing connections using three “P”s
  Persistent connections
  Parallel/concurrent connections
  Pipelined transfers over the same connection
Caching
  Forward proxy: close to clients
  Reverse proxy: close to servers
Replication

## Slide 30: Scorecard: Getting n small objects
Time dominated by latency
One-at-a-time: ~2n RTT
m concurrent: ~2[n/m] RTT
Persistent: ~ (n+1) RTT
Pipelined: ~2 RTT
Pipelined and Persistent: ~2 RTT first time; RTT later for another n from the same site

## Slide 31: Scorecard: Getting n large objects each of size F
Time dominated by TCP throughput BC (<= BL), where link bandwidth is referred by BL
One-at-a-time: ~ nF/BC
m concurrent: ~ nF/(mBC)
  Assuming each TCP connection gets the same throughput and mBC <= BL
Pipelined and/or persistent: ~ nF/BC
  The only thing that helps is higher throughput

## Slide 32: Content Distribution Networks (CDN)
Caching and replication as a service
Combination of caching and replication
  Pull: Direct result of clients’requests (caching)
  Push: Expectation of high access rate (replication)

## Slide 33: Hierarchies in the DNS
Three intertwined hierarchies
  Hierarchical namespace
    As opposed to flat namespace
  Hierarchically administered
    As opposed to centralized
  (Distributed) hierarchy of servers
    As opposed to centralized storage

## Slide 34: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers

## Slide 35: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 36: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 37: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 38: Name resolution: Recursive
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 39: Name resolution: Iterative
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?

## Slide 40: DNS caching
Performing all these queries takes time
  Up to 1-second latency before starting download
Caching can greatly reduce overhead
  The top-level servers very rarely change
  Popular sites (e.g., www.google.com) visited often
  Local DNS server often has the information cached
How DNS caching works
  DNS servers cache responses to queries
  Responses include a “time to live” (TTL) field
  Server deletes cached entry after TTL expires

## Slide 41: HTTP streaming
Video is stored at an HTTP server with a URL
Clients send a GET request for the URL
Server sends the video file as a stream
Client first buffers for a while to minimize interruptions later
Once the buffer reaches a threshold
  The video plays in the foreground
  More frames are downloaded in the background

## Slide 42: DASH : Dynamic Adaptive Streaming over HTTP
Keep multiple resolutions of the same video
  Stored in a manifest file in the HTTP server
Client asks for the manifest file first to learn about the options
Asks for chunks at a time and measures available bandwidth while they are downloaded
  Low bandwidth ⇒ switch to lower bitrate
  High bandwidth ⇒ switch to higher bitrate

## Slide 43: Applications
Common theme: parallelism
  Applications decomposed into tasks
  Running in parallel on different machines
Two common paradigms
  Partition-Aggregate
  Map-Reduce

## Slide 44: Traditional datacenter networks
Rack
Aggregation
Core

## Slide 45: Challenges
Not enough bandwidth
  Oversubscription: Less bandwidth in the ToR-Agg links than all the servers’ bandwidth in the rack
  Oversubscription ratio: Ratio between bandwidth underneath and bandwidth above
Not enough paths between server pairs
  Load balancing issues
  Failure recovery issues

## Slide 46: Modern datacenter networks: More bandwidth, more paths
Rack
Aggregation
Core

## Slide 47: Clos topology
Multi-stage network
k pods, where each pod has two layers of k/2 switches
  k/2 ports up and k/2 down
All links have the same b/w
At most k3/4 machines
Example
  k = 4
  16 machines
For k=48, 27648 machines
Pod 1
Pod 2
Pod 3
Pod 4

## Slide 48: Summary
We will focus on the transport layer from next class