## Slide 1: EECS 489 Computer Networks Fall 2020
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
From reliable data transfer to TCP
TCP connection setup and teardown

## Slide 3: Recap: Designing a reliable transport protocol
Stop and wait is correct but inefficient
Sliding window uses pipelining to increase throughput

## Slide 4: Recap: Acknowledgements
Cumulative
  Acknowledge many packets at a time
Selective
  Acknowledge individual packets

## Slide 5: Recap: Sliding window protocols
Resending packets: two canonical approaches
  Go-Back-N: Resend all N packets
  Selective Repeat: Resend only the missing packets
Many variants that differ in implementation details

## Slide 6: TCP: Transmission Control Protocol

## Slide 7: The TCP Abstraction
TCP delivers a reliable, in-order, byte stream
Reliable: TCP resends lost packets (recursively)
  Until it gives up and shuts down connection
In-order: TCP only hands consecutive chunks of data to application
Byte stream: TCP assumes there is an incoming stream of data, and attempts to deliver it to app

## Slide 8: What does TCP use from what we’ve seen so far?
Most of what we’ve seen
  Checksums
  Sequence numbers are byte offsets
  Sender and receiver maintain a sliding window
  Receiver sends cumulative acknowledgements (like GBN)
    Sender maintains a single retransmission timer
  Receivers buffer out-of-sequence packets (like SR)
Few more: fast retransmit, timeout estimation algorithms etc.

## Slide 9: Build the TCP header
Source port
Destination port
Data
Used to Mux
and Demux

## Slide 10: Build the TCP header
Source port
Destination port
Checksum
Data
Computed over pseudo-header
and data

## Slide 11: What does TCP do?
Most of what we’ve seen
  Checksum
  Sequence numbers are byte offsets

## Slide 12: Build the TCP header
Source port
Destination port
Sequence number
Checksum
Data
Byte offsets
(NOT packet id),
because TCP is a
byte stream

## Slide 13: TCP “stream of bytes” service…
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Application @ Host A
Application @ Host B
Byte 80
Byte 80

## Slide 14: … provided using TCP “segments”
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
TCP Data
TCP Data
Byte 80
Segment sent when:
Segment full (Max Segment Size),
Not full, but times out

## Slide 15: TCP segment
IP packet
  No bigger than Maximum Transmission Unit (MTU)
  E.g., up to 1500 bytes with Ethernet
TCP packet
  IP packet with a TCP header and data inside
  TCP header  20 bytes long
TCP segment
  No more than Maximum Segment Size (MSS) bytes
  E.g., up to 1460 consecutive bytes from the stream
  MSS = MTU – (IP header) – (TCP header)
IP Hdr
IP Data
TCP Hdr
TCP Data (segment)

## Slide 16: Sequence numbers
Host A
ISN (Initial Sequence Number)
Sequence number = 1st byte in segment = ISN + k
k bytes

## Slide 17: Sequence numbers
Host B
TCP Data
TCP Data
TCP
HDR
TCP
HDR
ACK sequence number
= next expected byte
= seqno + length(data)
Host A
ISN (Initial Sequence Number)
Sequence number = 1st byte in segment = ISN + k
k

## Slide 18: Build the TCP header
Source port
Destination port
Sequence number
Checksum
Data
Starting byte offset of data carried in this segment

## Slide 19: What does TCP do?
Most of what we’ve seen
  Checksum
  Sequence numbers are byte offsets
  Receiver sends cumulative acknowledgements (like GBN)

## Slide 20: ACKs and sequence numbers
Sender sends packet
  Data starts with sequence number X
  Packet contains B bytes [X, X+1, X+2, ….X+B-1]
Upon receipt of packet, receiver sends an ACK
  If all data prior to X already received:
    ACK acknowledges X+B (because that is next expected byte)
  If highest in-order byte received is Y s.t. (Y+1) < X
    ACK acknowledges Y+1
    Even if this has been ACKed before

## Slide 21: Typical operation
Sender: seqno=X, length=B
Receiver: ACK=X+B
Sender: seqno=X+B, length=B
Receiver: ACK=X+2B
Sender: seqno=X+2B, length=B
Seqno of next packet is same as last ACK field

## Slide 22: Build the TCP header
Source port
Destination port
Sequence number
Acknowledgment
Checksum
Data
Acknowledgment gives seqno just beyond highest seqno received in order

## Slide 23: What does TCP do?
Most of what we’ve seen
  Checksum
  Sequence numbers are byte offsets
  Receiver sends cumulative acknowledgements (like GBN)
  Receivers can buffer out-of-sequence packets (like SR)

## Slide 24: Loss with cumulative ACKs
Sender sends packets with 100B and seqnos.:
  100, 200, 300, 400, 500, 600, 700, 800, …
Assume the fifth packet (seqno 500) is lost, but no others
Stream of ACKs will be:
  200, 300, 400, 500, 500, 500, 500,…

## Slide 25: What does TCP introduce?
Most of what we’ve seen
  Checksum
  Sequence numbers are byte offsets
  Receiver sends cumulative acknowledgements (like GBN)
  Receivers can buffer out-of-sequence packets (like SR)
Introduces fast retransmit: duplicate ACKs trigger early retransmission

## Slide 26: Loss with cumulative ACKs
Duplicate ACKs are a sign of an isolated loss
  The lack of ACK progress means 500 hasn’t been delivered
  Stream of ACKs means some packets are being delivered
Trigger retransmission upon receiving k duplicate ACKs
    TCP uses k=3
    Faster than waiting for timeout

## Slide 27: Loss with cumulative ACKs
Two choices after resending
  Send missing packet and move sliding window by the number of dup ACKs
    Speeds up transmission, but might be wrong
  Send missing packet, and wait for ACK to move sliding window
    Is slowed down by single dropped packets
Which should TCP do?
  Choose correctness

## Slide 28: 5-minute break!

## Slide 29: Announcements
Assignment 2 is live!

## Slide 30: What does TCP introduce?
Most of what we’ve seen
  Checksum
  Sequence numbers are byte offsets
  Receiver sends cumulative acknowledgements (like GBN)
  Receivers buffer out-of-sequence packets (like SR)
Introduces fast retransmit: duplicate ACKs trigger early retransmission
Sender maintains a single retransmission timer (like GBN) and retransmits on timeout

## Slide 31: Retransmission timeout
If the sender hasn’t received an ACK by timeout, retransmit the first packet in the window
How do we pick a timeout value?
Notes: If the window moves, the timer is restarted

## Slide 32: Timing illustration
1
1
Timeout too long  inefficient
1
1
Timeout too short 
duplicate packets
RTT
Timeout
Timeout
RTT

## Slide 33: Retransmission timeout
If the sender hasn’t received an ACK by timeout, retransmit the first packet in the window
How to set timeout?
  Too long: connection has low throughput
  Too short: retransmit packet that was just delayed
Solution: make timeout proportional to RTT
  But how do we measure RTT?

## Slide 34: RTT estimation
Exponential weighted average of RTT samples
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT

## Slide 35: Problem: Ambiguous measurements
How do we differentiate between the real ACK, and ACK of the retransmitted packet?
ACK
Retransmission
Original Transmission
SampleRTT
Sender
Receiver
ACK
Retransmission
Original Transmission
SampleRTT
Sender
Receiver

## Slide 36: Karn/Partridge algorithm
Don’t use SampleRTT from retransmissions
  Once retransmitted, ignore that segment in the future
Computes EstimatedRTT using α = 0.125
Timeout value (RTO) = 2 × EstimatedRTT
  Employs exponential backoff
    Every time RTO timer expires, set RTO  2·RTO
      (Up to maximum  60 sec)
    Every time new measurement comes in (= successful original transmission), collapse RTO back to 2 × EstimatedRTT
Sensitive to RTT variations
Notes: 0.125 is 1/8, which is easier to compute by simple right shifting bits.

## Slide 37: Jacobson/Karels algorithm
Problem: need to better capture variability in RTT
  Directly measure deviation
Deviation = | SampleRTT – EstimatedRTT |
DevRTT: exponential average of Deviation
RTO = EstimatedRTT + 4 x DevRTT

## Slide 38: Build the TCP header
Source port
Destination port
Sequence number
Acknowledgment
HdrLen
0
Checksum
Urgent pointer
Data
Number of 4-byte words in the header;
5: No options

## Slide 39: TCP Connection Establishment

## Slide 40: Initial Sequence Number (ISN)
Sequence number for the very first byte
Why not just use ISN = 0?
  Practical issue
    IP addresses and port #s uniquely identify a connection
    Eventually, though, these port #s do get used again; small chance an old packet is still in flight
    Also, others might try to spoof your connection
  Why does using ISN help?
Hosts exchange ISNs when establishing connection

## Slide 41: Establishing a TCP connection
Three-way handshake to establish connection
  Host A sends a SYN (open; “synchronize sequence numbers”) to host B
  Host B returns a SYN acknowledgment (SYN ACK)
  Host A sends an ACK to acknowledge the SYN ACK
SYN
SYN ACK
ACK
A
B
Data
Data

## Slide 42: Build the TCP header
Source port
Destination port
Sequence number
Acknowledgment
HdrLen
Flags
0
Checksum
Urgent pointer
Data
Flags:
SYN
ACK
FIN
RST
PSH
URG

## Slide 43: Step 1: A’s initial SYN packet
A’s port
B’s port
A’s Initial Sequence Number
N/A
5
SYN
0
Checksum
Urgent pointer
A tells B to open a connection

## Slide 44: Step 1: B’s SYN-ACK packet
B’s port
A’s port
B’s Initial Sequence Number
ACK=A’s ISN+1
5
SYN|ACK
0
Checksum
Urgent pointer
B tells it accepts and is ready to accept next packet

## Slide 45: Step 1: A’s ACK to SYN-ACK
A’s port
B’s port
A’s Initial Sequence Number + 1
5
ACK
0
Checksum
Urgent pointer
A tells B to open a connection
ACK=B’s ISN+1

## Slide 46: TCP’s 3-Way handshaking
Client (initiator)
Server
SYN, SeqNum = x
SYN + ACK, SeqNum = y, Ack = x + 1
ACK, Ack = y + 1
Active Open
Passive Open
connect()
listen()

## Slide 47: What if the SYN Packet Gets Lost?
Suppose the SYN packet gets lost
  Packet dropped by the network or server is busy
Eventually, no SYN-ACK arrives
  Sender retransmits the SYN on timeout
How should the TCP sender set the timer?
  Sender has no idea how far away the receiver is
  Hard to guess a reasonable length of time to wait
  SHOULD (RFCs 1122 & 2988) use default of 3 seconds
    Some implementations instead use 6 seconds

## Slide 48: SYN loss and web downloads
User clicks on a hypertext link
  Browser creates a socket and does a “connect”
  The “connect” triggers the OS to transmit a SYN
If the SYN is lost…
  3-6 seconds of delay: can be very long
  User may become impatient and can retry
User triggers an “abort” of the “connect”
  Browser creates a new socket and another “connect”
  Can be effective in some cases

## Slide 49: TCP connection teardown

## Slide 50: Normal termination, one side at a time
Finish (FIN) to close and receive remaining bytes
  FIN occupies one byte in the sequence space
Other host acks the byte to confirm
Closes A’s side of the connection, but not B’s
  Until B likewise sends a FIN
  Which A then acks
SYN
SYN ACK
ACK
Data
FIN
ACK
ACK
time
A
B
FIN
ACK
TIME_WAIT:
Avoid reincarnation
B will retransmit FIN if ACK is lost
Connection now half-closed
Connection now closed
Notes: Why timer? Will get packet with no state!!

## Slide 51: Normal termination, both together
Same as before, but B sets FIN with their ack of A’s FIN
SYN
SYN ACK
ACK
Data
FIN
FIN + ACK
ACK
time
A
B
ACK
Connection now closed
TIME_WAIT:
Avoid reincarnation
Can retransmit FIN ACK if ACK lost

## Slide 52: Abrupt termination
A sends a RESET (RST) to B
  E.g., because application process on A crashed
That’s it
  B does not ack the RST
  Thus, RST is not delivered reliably, and any data in flight is lost
  But: if B sends anything more, will elicit another RST
SYN
SYN ACK
ACK
Data
RST
ACK
time
A
B
Data
RST

## Slide 53: Summary
Reliability is not easy!
Next
  Flow control
  LOTs of congestion control