## Slide 1: EECS 489 Computer Networks Fall 2020
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Topics
Network layer (lectures 12–16)
  Intra-domain routing
  Inter-domain routing
  SDN

## Slide 3: Network layer
Present everywhere
Performs addressing, forwarding, and routing, among other tasks
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch

## Slide 4: Forwarding vs. routing
Forwarding: “data plane”
  Directing one data packet
  Each router using local routing state
Routing: “control plane”
  Computing the forwarding tables that guide packets
  Jointly computed by routers using a distributed algorithm
Very different timescales!

## Slide 5: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
Control Plane
Data Plane

## Slide 6: Routing: Local vs. global view
Local routing state is the forwarding table in a single router
  By itself, the state in a single router cannot be evaluated
  It must be evaluated in terms of the global context
Global state refers to the collection of forwarding tables in each of the routers
  Global state determines which paths packets take

## Slide 7: “Valid” routing state
Global state is “valid” if it produces forwarding decisions that always deliver packets to their destinations
Goal of routing protocols: compute valid state
  How can we tell if routing state if valid?
Notes: What could go wrong?

## Slide 8: Necessary and sufficient condition
Global routing state is valid if and only if:
  There are no dead ends (other than destination)
  There are no loops
A dead end is when there is no outgoing link (next-hop)
  A packet arrives, but the forwarding decision does not yield any outgoing link
A loop is when a packet cycles around the same set of nodes forever

## Slide 9: Least-cost routes
Least-cost routes provide an easy way to avoid loops
  No reasonable cost metric is minimized by traversing a loop
Least-cost paths form a spanning tree for each destination rooted at that destination

## Slide 10: Intra-domain routing
Link-state (LS) routing protocol
  Dijkstra’s algorithm
  Broadcast neighbors’ info to everyone
Distance vector (DV) routing protocol
  Bellman-Ford algorithm
  Gossip to neighbors about everyone

## Slide 11: Link-state routing
Every router knows its local “link state”
  Router u: “(u,v) with cost=2; (u,x) with cost=1”
Each router floods its local link state to all other routers in the network
  Does so periodically or when its link state changes
Every router learns the entire network graph
  Each runs Dijkstra’s Shortest-Path First (SPF) algorithm locally to compute forwarding table

## Slide 12: Distance-vector protocol
Link-state routing protocol
  Each node broadcasts its local information
Distance-vector routing protocol
  The opposite (sort of)
  Each node tells its neighbors about its global view
Use Bellman-Ford equation

## Slide 13: Similarities between LS and DV routing
Both are shortest-path based routing
  Minimizing cost metric (link weights) a common optimization goal
    Routers share a common view as to what makes a path “good” and how to measure the “goodness” of a path
Due to shared goal, commonly used inside an organization
  RIP and OSPF are mostly used for intra-domain routing

## Slide 14: Comparison of LS and DV routing
Messaging complexity
LS: with N nodes, E links, O(NE) messages sent
DV: exchange between neighbors only
Speed of convergence
LS: relatively fast
DV: convergence time varies
  Count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  Node can advertise incorrect link cost
  Each node computes its own table
DV:
  Node can advertise incorrect path cost
  Each node’s table used by others (errors propagate)

## Slide 15: Inter-domain routing

## Slide 16: Autonomous systems (AS)
An AS is a network under a single administrative control
  Currently over 70,000 ASes
  Updated daily at http://www.cidr-report.org/as2.0/
ASes are sometimes called “domains”
Each AS is assigned a unique identifier (ASN)
  E.g., University of Michigan owns ASNs 177 to 180

## Slide 17: Addressing is key to scalable inter-domain routing
Ability to aggregate addresses is crucial for
  State: Small forwarding tables at routers
    Much less than the number of hosts
  Churn: Limited rate of change in routing tables

## Slide 18: Classful addressing
Three classes
  8-bit network prefix (Class A),
  16-bit network prefix (Class B), or
  24-bit network prefix (Class C)
Example: an organization needs 500 addresses.
  A single class C address is not enough (<500 hosts)
  Instead, a class B address is allocated (~65K hosts)
    Huge waste!

## Slide 19: CIDR: Classless inter-domain routing
Flexible division between network and host addresses
Offers a better tradeoff between size of the routing table and efficient use of the IP address space

## Slide 20: Allocation done hierarchically
Internet Corporation for Assigned Names and Numbers (ICANN) gives large blocks to…
Regional Internet Registries, such as the American Registry for Internet Names (ARIN), which give blocks to…
Large institutions (ISPs), which give addresses to…
Individuals and smaller institutions
FAKE Example:
  ICANN  ARIN  AT&T  UMICH  EECS

## Slide 21: Hierarchy in IP addressing
32 bits are partitioned into a prefix and suffix components
Prefix is the network component; suffix is the host component
Inter-domain routing operates on network prefix
00001100
00100010
10011110
00000101
Network (23 bits)
Host (9 bits)
12
34
158
5

## Slide 22: 5-minute break!

## Slide 23: Announcements
Prof. Jennifer Rexford will be giving a distinguished lecture on Nov 13 2:45-3:45PM
  Topic: Networks Capable of Change
  https://eecs.engin.umich.edu/event/networks-capable-of-change/

## Slide 24: Administrative structure shapes Inter-domain routing
ASes want freedom to pick routes based on policy
ASes want autonomy
ASes want privacy

## Slide 25: Business relationships
peer
peer
provider
customer
Relations between ASes
Customers pay provider
Peers don’t pay each other
Business implications

## Slide 26: Routing follows the money!
A
B
C
D
E
F
Q
Pr
Cu
Peer
Peer
traffic allowed
traffic not allowed
ASes provide “transit” between their customers
Peers do not provide transit between other peers

## Slide 27: BGP inspired by Distance-Vector with four differences
Shortest-path routes may not be picked to enforce policy
Path-Vector routing to avoid loops
Selective route advertisement may affect reachability
Routes may be aggregated for scalability

## Slide 28: BGP: Basic idea
Each AS selects the “best” route it hears advertised for a prefix
An AS advertises (“exports”) its best routes to one or more IP prefixes
Notes: Arrows are routing message

## Slide 29: Policy dictates how routes are “selected” and “exported”
Selection: Which path to use?
  Controls whether/how traffic leaves the network
Export: Which path to advertise?
  Controls whether/how traffic enters the network
Can reach 128.3/16
blah blah
Route selection
A
P
C
B
Q
Route export
Notes: Arrows: routing messages!

## Slide 30: Typical export policy
Destination prefix advertised by… | Export route to…
Customer | Everyone (providers, peers, other customers)
Peer | Customers
Provider | Customers
We’ll refer to these as the “Gao-Rexford” rules
(capture common – but not required! – practice)

## Slide 31: Selection using attributes
Rules for route selection in priority order
Priority | Rule | Remarks
1 | LOCAL PREF | Pick highest LOCAL PREF
2 | ASPATH | Pick shortest ASPATH length
3 | MED | Lowest MED preferred
4 | eBGP > iBGP | Did AS learn route via eBGP (preferred) or iBGP?
5 | iBGP path | Lowest IGP cost to next hop (egress router)
6 | Router ID | Smallest next-hop router’s IP address as tie-breaker

## Slide 32: Who speaks BGP?
Border router
Border routers in an Autonomous System
Internal router

## Slide 33: eBGP, iBGP, and IGP
eBGP: BGP sessions between border routers in different ASes
  Learn routes to external destinations
iBGP: BGP sessions between border routers and other routers within the same AS
  Distribute externally learned routes internally
IGP: “Interior Gateway Protocol” = Intra-domain routing protocol
  Provide internal reachability via shortest path
  E.g., OSPF, RIP

## Slide 34: Software-defined and programmable networks

## Slide 35: “The Power of Abstraction”
“Modularity based on abstraction is the way things get done”
  Barbara Liskov
Abstractions  Interfaces  Modularity

## Slide 36: Separate concerns with abstractions
Be compatible with low-level hardware/software
  Need an abstraction for general forwarding model
Make decisions based on entire network
  Need an abstraction for network state
Compute configuration of each physical device
  Need an abstraction that simplifies configuration

## Slide 37: Traditional fully decentralized control plane
Individual routing algorithm components in every router interact in the control plane
111010010
MIT
Dst | Next Hop
UMICH | 0
UCB | 0
MIT | 0
NYU | 0
Control
Plane
Data
Plane

## Slide 38: Logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs)
111010010
MIT
Dst | Next Hop
UMICH | 0
UCB | 0
MIT | 0
NYU | 0
Control
Plane
Data
Plane
Remote Control

## Slide 39: SDN: Many challenges remain
Hardening the control plane: dependable, reliable, performance-scalable, secure distributed system
  Robustness to failures: leverage strong theory of reliable distributed system for control plane
  Security: “baked in” from day one?
Networks, protocols meeting mission-specific requirements
  E.g., real-time, ultra-reliable, ultra-secure
Internet-scaling

## Slide 40: OpenFlow data plane abstraction
Flow is defined by header fields
Generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller

## Slide 41: Fixed-function data plane
Traditional switches are fixed-function
  They can do whatever they can do at birth, but they cannot change!
  Bottom-up design
Even OpenFlow was designed to be a fixed protocol
  With a fixed table format
  Capable of doing limited things

## Slide 42: Programmable data plane
What if we could tell switches exactly what we want?
  What table to keep?
  What rules to use?
  What data to keep track of?
  …

## Slide 43: Top-down workflow
Precisely specify using a well-defined language
Compile it down to run on a standardized hardware (e.g., using P4)
Run at line speed

## Slide 44: PISA: Protocol Independent Switch Architecture
Match + Action
Memory
ALU
Programmable
Parser
Programmer declares which
headers are recognized
Programmer declares what
tables are needed and how packets are processed
All stages are identical – makes PISA a good “compiler target”

## Slide 45: Summary
Intra-domain routing minimizes a cost metric
Inter-domain routing is more complex due to policies
Programmable networks are more flexible than fixed-function ones
Next week: Layer 2
Join us on Friday in welcoming Prof. Jen Rexford back to Michigan for a DLS talk